Zylin CPU
Øyvind Harboe, General Manager, Zylin AS

---
Motivation
Provide a 32 bit core with standard tools while taking up a minimum of real estate
Flexible core and architecture that can be used with any FPGA brand/type, memory and IO subsystem
Leave FPGA resources to HDL paradigm

---
What the ZPU is not
Not ARM9, XScale, etc. type CPU
Not for sustained processing
Not for running Linux – no MMU
Unlikely to run uCLinux

---
ZPU - performance
DMIPS – popular performance index for deeply embedded processors
Easy to measure with working GCC and Dhrystone v2.1
1 – 10 DMIPS depending configuration and memory subsystem
The ZPU is for light administrative tasks
The ZPU punches above its weight
  - Leaves resources to HDL paradigm
  - eCos performance tests are relatively better and more relevant

---
ZPU – real estate
LUT - FPGA MIPS. A popular index of real estate usage
Must be measured using actual tools and part
Xilinx XC3S400 – 440 LUT with 32 bit data path

---
ZPU - codesize
80% of ARM7 Thumb. Measured on eCos applications.
There exists no MIPS equivalent for code size

---
ZPU programming model
Standard programming model
A single linear 32 bit address space
Unused address bits are optimized away by synthesis optimisation
IO is memory mapped

---
GCC toolchain
GCC
GDB
newlib/libgloss – OS less applications
Zylin Embedded CDT debug GUI

---
SoPC
System On a Programmable Chip
ZPU core running
    - eCos
    - Applications and drivers (TCP/IP, Flash-file system,...)
Memory interfaces (Internal/external memory)
Peripheral interface/controllers
    - Ethernet MAC (opencores)
    - Standard 16550 or simple UARTs (opencores)
    - DDR SDRAM controller (Zylin)
    - I2C, USB, SDIO, GPIO.......

---
eCos – RTOS Real Time OS
eCos – open source free deeply embedded operating system
  - eCos is not Linux
  - Small footprint
  - TCP/IP
  - USB function drivers
  - Flash drivers
  - GDB stubs – target debugging via simple UART
  - The list goes on and on
  - eCos is the rising star for deeply embedded

---
eCos HAL
A ZPU comes with a variant eCos HAL configured to a ZPU port and peripherals
Special drivers? Drivers are CPU independent.
Opencores ethermac driver runs unmodified on SPARC, ARM and the ZPU
Check eCos repository for your peripherals/driver stack

---
ZPU HDL
ZPU's key strength is small footprint
Starts at 300-500 LUT
16/32 bit datapath
Core choice depends on memory and IO subsystem
Dual port, single port, wishbone, custom

---
Custom ZPU
Size optimisation for particular memory and IO subsystem
More instructions? There are various instructions that can be enabled and disabled without changing compiler or binaries
Even more instructions? May require GCC support
Special machine code only instructions? Instructions tightly integrated with peripherals?
Peripherals?

---
ISS – instruction set simulator
Simulates ZPU to run binaries from GCC
Takes simulator trace output for verification and cycle accurate statistics/debugging
GDB server interface
Simple peripheral simulation – timer, UART, etc.
Does not replace debugging real target
Custom ZPU verification/profiling
Early development/training before target PCB is available
Used for debugging eCos HAL

---
ZPU – roadmap
Stay away from 50-500 DMIPS range
Reduce footprint – obviously not a large potential
Performance increases without sacrificing area or code density
Improve code density – possibly at FPGA resource cost, SRAM and flash is real-estate too
Improve GCC code quality
Improve debug tools
Optional peripherals?

---
ZPU – summary
1-10 MIPS
16 or 32 datapath
Codesize 80% of ARM7 Thumb
GCC toolchain
eCos HAL
Various HDL cores available
400 LUTs – 32 bit datapath

---
Questions?