# ZPU - Zylin Soft CPU
Prototype architecture

Whitepaper

V1.5

April 4. 2005
Copyright  2005, Zylin AS
oyvind.harboe@zylin.com

Abstract

This white paper describes the the architecture of the ZPU prototype. The purpose of the prototype is to establish FPGA real-estate size and lower performance range of the ZPU and finally to give feedback to the compiler development.

Although the architecture has been optimised for simplicity of implementation and to be reasonably well adapted to the GCC toolchain alpha version available at the time of start for the prototype project, it should in important respects approximate the minimum FPGA real-estate ZPU profile.

# Stack
The ZPU is a stack based architecture. The stack behaves as most stacks do on modern CPUs.

- The SP register points to the value on top of the stack.
- Pushes predecrement the stack pointer, then store the value on top of the stack
- Pops are postincrement

# Registers
Register name	Description
PC	Contains enough bits to address entire RAM and IO mapped memory.
SP	Contains enough bits to address entire RAM. Bit 0 and 1 are always 0.

# Instruction set
Only the base instructions are implemented in the architecture. More advanced instructions, like ASHIFTLEFT are emulated in the illegal instruction vector.

All operations are 32 bit wide.

Name	Opcode	Action
BREAKPOINT	000x 0000	The debugger sets a memory location to this value to set a breakpoint. Once a JTAG-like debugger interface is added, it will be convenient to be able to distinguish between a breakpoint and an illegal(possibly emulated) instruction.
IM	1xxx xxxx	Pushes 7 bit sign extended integer and sets the a «instruction decode interrupt mask» flag(IDIM). / If the IDIM flag is already set, this instruction shifts the value on the stack left by 7 bits and stores the 7 bit immediate value into the lower 7 bits. / Unless an instruction is listed as treating the IDIM flag specially, it should be assumed to clear the IDIM flag. / To push a 14 bit integer onto the stack, use two consequtive IM instructions. / If multiple immediate integers are to be pushed onto the stack, they must be interleaved with another instruction.
STORESP	010x xxxx	Pop value off stack and store it in the SP+xxxxx*4 memory location, where xxxxx is a positive integer.
LOADSP	011x xxxx	Push value of memory location SP+xxxxx*4, where xxxxx is a positive integer, onto stack.
EMULATE	001x xxxx	Push PC to stack and set PC to 0x0+xxxxx*32. This is used to emulate opcodes.
PUSHPC	000x 0001	Pushes program counter onto the stack.
POPPC	000x 0100	Pops address off stack and sets PC
LOAD	000x 1000	Pops address stored on stack and loads the value of that address onto stack. / Bit 0 and 1 of address are always 0.
STORE	000x 1100	Pops address, then value from stack and stores the value into the memory location of the address. / Bit 0 and 1 of address are always 0
PUSHSP	000x 0010	Pushes stack pointer.
POPSP	000x 1101	Used to allocate/deallocate space on stack for variables or when changing threads.
ADD	000x 0101	Pops two values on stack adds them and pushes the result
AND	000x 0110	Pops two values off the stack and does a bitwise-and & pushes the result onto the stack
OR	000x 0111	Pops two integers, does a bitwise or and pushes result
NOT	000x 1001	Bitwise inverse of value on stack
FLIP	000x 1010	Reverses the bit order of the value on the stack, i.e. abc->cba, 100->001, 110->011, etc.
NOP	000x 1011	No operation
UNDEFINED	000x 0011
UNDEFINED	000x 1110
UNDEFINED	000x 1111

# Vectors
Address	Name	Description
0x000	Reset	When the ZPU boots, this is the first instruction to be executed. / The stack pointer is initialised to maximum RAM address
0x020	Interrupt(future)	This is the entry point for interrupts. Not implemented yet, but used by the simulator when running eCos.
0x040-	Emulated instruction	Emulated opcode 34. Note that opcode 32 and opcode 33 are not normally used to emulate instructions as these memory addresses are already used by boot vector, GCC registers and the interrupt vector.

# Memory map
Bit 30-13 inclusive are ignored by the ZPU.

Start address	To-address	Description
0x00000000	0x00000100	Reserved for compiler and operating system usage. / The alpha version of the compiler simulates GCC registers by using low-memory locations. The final version of the compiler will place GCC registers in the stack frame. / Note here the distinction between GCC registers and ZPU registers. There are no corresponding arithmetic/address ZPU hardware registers.
0x00000100	0x00000200	Traps
0x00000200	0x00004000	Memory for application and data.
0x80000000	0x80000100	IO registers

# IO registers
Name	Description
Read-char	Reads a char from a serial line FIFO. 0 if no char is available.
Write-char	Writes a char to a serial line.
Clock-counter	A clock counter that increases by one for each cycle. Used for timing applications, etc.

# Optimisations
The ZPU programming model allows certain shortcuts to be taken.

Optimisations	Description
Discard stack data	When a value is popped from the stack, it is no longer necessary to persist that value to memory. This can be significant in ZPU implementations that have a stack cache unit that has write back to memory.